CONVERSION TABLES
OIL
Amount	Quantity in Common Use	Abbreviation	=	Equivalent	Explanation
			=

GAS

Amount	Quantity in Common Use	Abbreviation	=	Equivalent	Explanation
			=
1	Standard Cubic Meter	SCM	=	1 cubic metre @ NTP	1 atmosphere pressure ( 14.7 ibs/sq inch ) and 15° C
1	Cubic Metre	M3	=	35.3 Cubic Feet
1	Billion Cubic Metre/Yr	BCM/Yr	=	2.8 MMSCD
1	Trillion Cubic Feet	TCF	=	4 MMSCMD	3.88 MMSCMD (100% recoverable (20yrs x 365days)
1	Million Tonne Per Annum(LNG)	MMTPA(LNG)	=	4 MMSCMD	3.60 MMSCMD (Mol Wt. of 18 @365days/annum
1	MT of LNG		=	1300 SCM	1314 SCM(Mol. Wt. 18)
	Gross Calorific Value	GCV	=	1000 Kcal/SCM
	Net Calorific Value	NCV	=	90% of GCV
1	Million BTU	MMBTU	=	25.2 SCM	GCV 10000 Kcal/SCM
1	Mega Watt of Power require	MW	=	4500 SCMD	4440 @ Heat Rate 1850 Kcal/Kwh
	Power from 1 MMSCMD Gas		=	220 MW
	Specific Gravity of Gas		=	0.65
	Density of Gas		=	0.76 Kg/SCM